Key Management Interoperability Protocol Use Cases Version 1.0

Committee Draft 05 / Public Review 01

05 November 2009

Specification URIs:

This Version:

http://docs.oasis-open.org/kmip/usecases/v1.0/cd05/kmip-usecases-1.0-cd-05.html

http://docs.oasis-open.org/kmip/usecases/v1.0/cd05/kmip-usecases-1.0-cd-05.doc  (Authoritative)

http://docs.oasis-open.org/kmip/usecases/v1.0/cd05/kmip-usecases-1.0-cd-05.pdf

Previous Version:

N/A

Latest Version:

http://docs.oasis-open.org/kmip/usecases/v1.0/kmip-usecases-1.0.html

http://docs.oasis-open.org/kmip/usecases/v1.0/kmip-usecases-1.0.doc

http://docs.oasis-open.org/kmip/usecases/v1.0/kmip-usecases-1.0.pdf

Technical Committee:

OASIS Key Management Interoperability Protocol (KMIP) TC

Chair(s):

Robert Griffin, EMC Corporation <robert.griffin@rsa.com>

Subhash Sankuratripati, NetApp <Subhash.Sankuratripati@netapp.com>

Editor(s):

Mathias Björkqvist, IBM <mbj@zurich.ibm.com>

René Pawlitzek, IBM <rpa@zurich.ibm.com>

Related work:

This specification replaces or supersedes:

None

This specification is related to:

Key Management Interoperability Protocol Specification Version 1.0

Key Management Interoperability Protocol Profiles Version 1.0

Key Management Interoperability Protocol Usage Guide Version 1.0

Abstract:

This document is intended for developers and architects who wish to design systems and applications that interoperate using the Key Management Interoperability Protocol specification.

Status:

This document was last revised or approved by the Key Management Interoperability Protocol TC on the above date. The level of approval is also listed above. Check the “Latest Version” or “Latest Approved Version” location noted above for possible later revisions of this document.

Technical Committee members should send comments on this specification to the Technical Committee’s email list. Others should send comments to the Technical Committee by using the “Send A Comment” button on the Technical Committee’s web page at http://www.oasis-open.org/committees/kmip/.

For information on whether any patents have been disclosed that may be essential to implementing this specification, and any offers of patent licensing terms, please refer to the Intellectual Property Rights section of the Technical Committee web page (http://www.oasis-open.org/committees/kmip/ipr.php).

The non-normative errata page for this specification is located at http://www.oasis-open.org/committees/kmip/.

Notices

Copyright © OASIS® 2009. All Rights Reserved.

All capitalized terms in the following text have the meanings assigned to them in the OASIS Intellectual Property Rights Policy (the "OASIS IPR Policy"). The full Policy may be found at the OASIS website.

This document and translations of it may be copied and furnished to others, and derivative works that comment on or otherwise explain it or assist in its implementation may be prepared, copied, published, and distributed, in whole or in part, without restriction of any kind, provided that the above copyright notice and this section are included on all such copies and derivative works. However, this document itself may not be modified in any way, including by removing the copyright notice or references to OASIS, except as needed for the purpose of developing any document or deliverable produced by an OASIS Technical Committee (in which case the rules applicable to copyrights, as set forth in the OASIS IPR Policy, must be followed) or as required to translate it into languages other than English.

The limited permissions granted above are perpetual and will not be revoked by OASIS or its successors or assigns.

This document and the information contained herein is provided on an "AS IS" basis and OASIS DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY WARRANTY THAT THE USE OF THE INFORMATION HEREIN WILL NOT INFRINGE ANY OWNERSHIP RIGHTS OR ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE.

OASIS requests that any OASIS Party or any other party that believes it has patent claims that would necessarily be infringed by implementations of this OASIS Committee Specification or OASIS Standard, to notify OASIS TC Administrator and provide an indication of its willingness to grant patent licenses to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification.

OASIS invites any party to contact the OASIS TC Administrator if it is aware of a claim of ownership of any patent claims that would necessarily be infringed by implementations of this specification by a patent holder that is not willing to provide a license to such patent claims in a manner consistent with the IPR Mode of the OASIS Technical Committee that produced this specification. OASIS may include such claims on its website, but disclaims any obligation to do so.

OASIS takes no position regarding the validity or scope of any intellectual property or other rights that might be claimed to pertain to the implementation or use of the technology described in this document or the extent to which any license under such rights might or might not be available; neither does it represent that it has made any effort to identify any such rights. Information on OASIS' procedures with respect to rights in any document or deliverable produced by an OASIS Technical Committee can be found on the OASIS website. Copies of claims of rights made available for publication and any assurances of licenses to be made available, or the result of an attempt made to obtain a general license or permission for the use of such proprietary rights by implementers or users of this OASIS Committee Specification or OASIS Standard, can be obtained from the OASIS TC Administrator. OASIS makes no representation that any information or list of intellectual property rights will at any time be complete, or that any claims in such list are, in fact, Essential Claims.

The names "OASIS", “KMIP” are trademarks of OASIS, the owner and developer of this specification, and should be used only to refer to the organization and its official outputs. OASIS welcomes reference to, and implementation and use of, specifications, while reserving the right to enforce its marks against misleading uses. Please see http://www.oasis-open.org/who/trademark.php for above guidance.

Table of Contents

1	Introduction	5

1.1	Normative References	5

2	Message exchange	6

3	Centralized Management	7

3.1	Basic functionality	7

3.1.1	Use-case: Create / Destroy	7

3.1.2	Use-case: Register / Create / Get attributes / Destroy	9

3.1.3	Use-case: Create / Locate / Get / Destroy	15

3.1.4	Use-case: Dual client use-case, ID Placeholder linked Locate & Get batch	20

3.2	Use-case: Asynchronous Locate	34

4	Key life cycle support	45

4.1	Use-case: Revoke scenario	45

5	Auditing and reporting	62

5.1	Use-case: Get usage allocation scenario	62

6	Key Interchange, Key Exchange	74

6.1	Use-case: Import of a Third-party Key	74

7	Vendor Extensions	79

7.1	Use-case: Unrecognized Message Extension with Criticality Indicator false	79

7.2	Use-case: Unrecognized Message Extension with Criticality Indicator true	79

8	Asymmetric keys	80

8.1	Use-case: Create a Key Pair	80

8.2	Use-case: Register Both Halves of a Key Pair	80

9	Key Roll-over	82

9.1	Use-case: Create a Key, Re-key	82

9.2	Use-case: Existing Key Expired, Re-key with Same lifecycle	83

9.3	Use-case: Existing Key Compromised, Re-key with same lifecycle	84

9.4	Use-case: Create key, Re-key with new lifecycle	85

9.5	Use-case: Obtain Lease for Expired Key	85

10	Archival	88

10.1	Use-case: Create a Key, Archive and Recover it	88

11	Implementation Conformance	90

A.	Acknowledgments	91

B.	Revision History	93

# Introduction

The purpose of this document is to describe use-cases to demonstrate the Key Management Interoperability Protocol (KMIP) [KMIP-Spec]. The use-cases indicate if all concepts within the protocol are sound and if the protocol is usable when implementing typical scenarios in real life. These use-cases are not intended to fully test an implementation of KMIP. Thus, the use-cases do not contain typical QA scenarios which would stress an implementation. The use-cases are based on v1.0 of the protocol.

The use-cases define a number of client-to-server request-response pairs for a number of operations. For each request-response message pair the operation is stated, along with the relevant parameters needed for the request or response message. This is followed by two different illustrations of the messages: first, a human-readable construction which shows the fields tags, types and values, followed by the TTLV-encoding of the message. These are included to facilitate the implementation of the message creation and parsing functionality. The use-cases show one possible way to construct the messages, and the messages shown are not necessarily the only correct constructions (e.g. it is possible to omit the attribute index if it is zero). Also note that many values change dynamically when running the use-cases (the server-generated timestamps, Unique Identifiers and key material in responses, as well as Batch Item ID values in client-generated requests).

## Normative References

[KMIP-Spec]	OASIS Committee Draft 06, Key Management Interoperability Specification Version 1.0, November 2009. http://docs.oasis-open.org/kmip/spec/v1.0/cd06/kmip-spec-1.0-cd-06.doc

[KMIP-Prof]	OASIS Committee Draft 04, Key Management Interoperability Protocol Profiles Version 1.0, November 2009. http://docs.oasis-open.org/kmip/profiles/v1.0/cd04/kmip-profiles-1.0-cd-04.doc

# Message exchange

The message exchange between clients and the server to test the following use-case scenarios is performed with TTLV encoding over the http transport. This is to facilitate debugging and to focus on KMIP-specific issues instead of potential secure transport setup problems.

# Centralized Management

## Basic functionality

These use-cases test the basic features of KMIP including key creation and template registration, attribute functionality, access methods, and batch operation.

### Use-case: Create / Destroy

In this use-case the client issues a Create request, whereby the server creates a new symmetric key and returns the Unique Identifier. To clean up, the client then performs a Destroy operation to destroy the key.

| Time | Request/Response messages |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’ (Symmetric Key), attributes={ CryptographicAlgorithm=’00000003’ (AES), CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x0000000C (Encrypt, Decrypt) 420075010000012042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F01000000D842005A0500000004000000010000000042007601000000C04200550500000004000000020000000042008E01000000A8420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000C00000000 Out: objectType=’00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0731C (Mon Sep 28 10:26:04 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 46eca90a-4b20-423c-b968-750f299f0ca7 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0731C42000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002434366563613930612D346232302D343233632D623936382D37353066323939663063613700000000 |
| 1 | Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 46eca90a-4b20-423c-b968-750f299f0ca7 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002434366563613930612D346232302D343233632D623936382D37353066323939663063613700000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0731D (Mon Sep 28 10:26:05 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 46eca90a-4b20-423c-b968-750f299f0ca7 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0731D42000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002434366563613930612D346232302D343233632D623936382D37353066323939663063613700000000 |

### Use-case: Register / Create / Get attributes / Destroy

Here the client first registers a template object and then creates a symmetric key using the registered template. To verify that the attributes of the key were set correctly from the template, the client then issues a Get Attributes command, after which it destroys first the key and then the template.

| Time | Request/Response messages |
| --- | --- |
| 0 | Register (template) In: objectType=’00000007’, attributes={ ObjectGroup=’Group1’, ApplicationSpecificInformation=’ssl, www.example.com’, ContactInformation=’Joe’, x-Purpose=’demonstration’, Name={ NameValue=’Template1’, NameType=’00000001’ } } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000006 (Template) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Group Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Group1 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Application Specific Information Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Application Namespace (0x420003), Type: Text String (0x07), Data: ssl Tag: Application Data (0x420002), Type: Text String (0x07), Data: www.example.com Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Joe Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-Purpose Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: demonstration Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Template1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000001C042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000017842005A0500000004000000030000000042007601000001604200550500000004000000060000000042008E0100000148420008010000002842000A070000000C4F626A6563742047726F75700000000042000B070000000647726F7570310000420008010000005842000A07000000204170706C69636174696F6E20537065636966696320496E666F726D6174696F6E42000B0100000028420003070000000373736C0000000000420002070000000F7777772E6578616D706C652E636F6D00420008010000003042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000B07000000034A6F650000000000420008010000003042000A0700000009782D507572706F73650000000000000042000B070000000D64656D6F6E7374726174696F6E000000420008010000004042000A07000000044E616D650000000042000B0100000028420053070000000954656D706C617465310000000000000042005205000000040000000100000000 Out: uuidTemplate Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0731E (Mon Sep 28 10:26:06 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fc3f473-4de4-4248-990e-21e00f7fc006 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0731E42000D0200000004000000010000000042000F010000005842005A0500000004000000030000000042007C050000000400000000000000004200790100000030420091070000002434666333663437332D346465342D343234382D393930652D32316530306637666330303600000000 |
| 1 | Create (symmetric key using template) In: objectType=’00000002’, template={ NameValue=’Template1’, NameType=’00000001’ }, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Name (0x420051), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Template1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x0000000C (Encrypt, Decrypt) 420075010000015042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000010842005A0500000004000000010000000042007601000000F04200550500000004000000020000000042008E01000000D84200510100000028420053070000000954656D706C617465310000000000000042005205000000040000000100000000420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000C00000000 Out: objectType=’00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0731F (Mon Sep 28 10:26:07 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 300881c8-596a-48ad-814f-7ce119896608 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0731F42000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002433303038383163382D353936612D343861642D383134662D37636531313938393636303800000000 |
| 2 | Get attributes In: uuidKey, attributeNames={‘ObjectGroup’, ‘ApplicationSpecificInformation’, ‘ContactInformation’, ‘x-Purpose’} Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 300881c8-596a-48ad-814f-7ce119896608 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Group Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Application Specific Information Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-Purpose 420075010000010842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F01000000C042005A05000000040000000B0000000042007601000000A8420091070000002433303038383163382D353936612D343861642D383134662D3763653131393839363630380000000042000A070000000C4F626A6563742047726F75700000000042000A07000000204170706C69636174696F6E20537065636966696320496E666F726D6174696F6E42000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000A0700000009782D507572706F736500000000000000 Out: uuidKey, attributes={ ObjectGroup=’Group1’, ApplicationSpecificInformation=’ssl, www.example.com’, ContactInformation=‘Joe Miller’, x-Purpose=’demonstration’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0731F (Mon Sep 28 10:26:07 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 300881c8-596a-48ad-814f-7ce119896608 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Group Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Group1 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Application Specific Information Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Application Namespace (0x420003), Type: Text String (0x07), Data: ssl Tag: Application Data (0x420002), Type: Text String (0x07), Data: www.example.com Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Joe Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-Purpose Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: demonstration 42007801000001B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0731F42000D0200000004000000010000000042000F010000015842005A05000000040000000B0000000042007C050000000400000000000000004200790100000130420091070000002433303038383163382D353936612D343861642D383134662D37636531313938393636303800000000420008010000002842000A070000000C4F626A6563742047726F75700000000042000B070000000647726F7570310000420008010000005842000A07000000204170706C69636174696F6E20537065636966696320496E666F726D6174696F6E42000B0100000028420003070000000373736C0000000000420002070000000F7777772E6578616D706C652E636F6D00420008010000003042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000B07000000034A6F650000000000420008010000003042000A0700000009782D507572706F73650000000000000042000B070000000D64656D6F6E7374726174696F6E000000 |
| 3 | Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 300881c8-596a-48ad-814f-7ce119896608 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002433303038383163382D353936612D343861642D383134662D37636531313938393636303800000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07320 (Mon Sep 28 10:26:08 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 300881c8-596a-48ad-814f-7ce119896608 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732042000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002433303038383163382D353936612D343861642D383134662D37636531313938393636303800000000 |
| 4 | Destroy (template) In: uuidTemplate Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fc3f473-4de4-4248-990e-21e00f7fc006 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002434666333663437332D346465342D343234382D393930652D32316530306637666330303600000000 Out: uuidTemplate Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07320 (Mon Sep 28 10:26:08 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fc3f473-4de4-4248-990e-21e00f7fc006 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732042000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002434666333663437332D346465342D343234382D393930652D32316530306637666330303600000000 |

### Use-case: Create / Locate / Get / Destroy

This use-case tests the Locate and Get operations, in addition to the previously used operations Create and Destroy. A symmetric key is first created, and then a lookup is performed on the Name attribute using the Locate operation. Subsequently, a Get request is issued to retrieve the located key, after which the key on the server is destroyed.

| Time | Request/Response messages |
| --- | --- |
| 0 | Create (symmetric key) In: objectType = ‘00000002’, attributes={ Name={ NameValue=‘Key1’, NameType=’00000001’ }, CryptographicAlgorithm=’DES’, CryptographicLength=’56’, CryptographicUsageMask=‘0000000C’, ContactInformation=’Joe’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000001 (DES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000038 (56) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x0000000C (Encrypt, Decrypt) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Joe 420075010000019842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000015042005A0500000004000000010000000042007601000001384200550500000004000000020000000042008E0100000120420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000100000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000003800000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000C00000000420008010000003042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000B07000000034A6F650000000000 Out: objectType = ‘00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07321 (Mon Sep 28 10:26:09 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732142000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 |
| 1 | Locate (symmetric key) In: attributes={ objectType = ‘00000002’, Name={ Name=‘Key1’, NameType=’00000001’} } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000D042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07321 (Mon Sep 28 10:26:09 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732142000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 |
| 2 | Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 Out: objectType = ‘00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07322 (Mon Sep 28 10:26:10 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: EAD09734B085DFFE Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000001 (DES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000038 (56) 420078010000011842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732242000D0200000004000000010000000042000F01000000C042005A05000000040000000A0000000042007C05000000040000000000000000420079010000009842005505000000040000000200000000420091070000002437356461396263392D373836372D343963352D383836642D3735376633643532336433660000000042008C010000005042003E01000000484200400500000004000000010000000042004301000000104200410800000008EAD09734B085DFFE4200260500000004000000010000000042002802000000040000003800000000 |
| 3 | Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07322 (Mon Sep 28 10:26:10 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732242000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 |
| 4 | Locate In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Unique Identifier Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: 75da9bc9-7867-49c5-886d-757f3d523d3f 42007501000000B842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000007042005A050000000400000008000000004200760100000058420008010000005042000A0700000011556E69717565204964656E7469666965720000000000000042000B070000002437356461396263392D373836372D343963352D383836642D37353766336435323364336600000000 Out: <empty response payload> Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07323 (Mon Sep 28 10:26:11 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: null 420078010000008042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732342000D0200000004000000010000000042000F010000002842005A0500000004000000080000000042007C050000000400000000000000004200790100000000 |

### Use-case: Dual client use-case, ID Placeholder linked Locate & Get batch

This use-case has two clients performing operations on the same key. The first client initially registers a template and creates a symmetric key using that template. The second client then does a batched Locate and Get using the ID Placeholder to retrieve the key. The second client thereafter performs a number of operations on the key (Get Attribute List, Get Attribute, Add Attribute, Modify Attribute and Delete Attribute), before the first client finally destroys the key and the template. The first client also tries to Get the key and the template after they have been destroyed, but the Get operation fails in both cases.

This use-case demonstrates the fact that it is possible for two clients to cooperate and use the same managed object while only having knowledge of a single pre-agreed Name attribute value and without having to share any other information. Here, the identities of the two clients are not considered and since we do not include an Authentication field in the header, they could also be considered to be the same client. If the clients authenticate themselves to the server using different credentials, the server needs to employ another policy than the Default policy defined in the KMIP specification on the key object to allow both clients to access it.

| Time | Request/Response messages |
| --- | --- |
| 0 | Client A: Register (template) In: objectType=’00000007’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, Name={ NameValue=’Template1’, NameType=’00000001’ },} Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000006 (Template) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Template1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 420075010000013042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F01000000E842005A0500000004000000030000000042007601000000D04200550500000004000000060000000042008E01000000B8420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000004042000A07000000044E616D650000000042000B0100000028420053070000000954656D706C617465310000000000000042005205000000040000000100000000 Out: uuidTemplate Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07323 (Mon Sep 28 10:26:11 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8383198b-4600-4388-955f-2802cc699e9c 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732342000D0200000004000000010000000042000F010000005842005A0500000004000000030000000042007C050000000400000000000000004200790100000030420091070000002438333833313938622D343630302D343338382D393535662D32383032636336393965396300000000 |
| 1 | Client A: Create (symmetric key using template) In: objectType=’00000002’, template={ NameValue= ‘Template1’, NameType=’00000001’ }, attributes={ Name={ Name=‘Key1’, NameType=’00000001’ }, CryptographicUsageMask=‘00000004’, ContactInformation=‘Foo’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Name (0x420051), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Template1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000004 (Encrypt) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Foo 420075010000015842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000011042005A0500000004000000010000000042007601000000F84200550500000004000000020000000042008E01000000E04200510100000028420053070000000954656D706C617465310000000000000042005205000000040000000100000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000400000000420008010000003042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000B0700000003466F6F0000000000 Out: objectType=’00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07324 (Mon Sep 28 10:26:12 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732442000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000 |
| 2 | Client B: Locate and Get (symmetric key by name) In (header): batchOrderOption=’TRUE’ In: attributes={ objectType = ‘00000002’, Name={ Name=‘Key1’, NameType=’00000001’} } In: <empty Get payload> Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Order Option (0x420010), Type: Boolean (0x06), Data: TRUE Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 01F76942FF5A7A8A Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3192EDD439D59CC4 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: null 42007501000001204200740100000048420067010000002042006802000000040000000100000000420069020000000400000000000000004200100600000008000000000000000142000D0200000004000000020000000042000F010000009842005A05000000040000000800000000420090080000000801F76942FF5A7A8A4200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B657931000000004200520500000004000000010000000042000F010000002842005A05000000040000000A0000000042009008000000083192EDD439D59CC44200760100000000 Out: uuidKey Out: objectType=’00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07324 (Mon Sep 28 10:26:12 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 01F76942FF5A7A8A Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3192EDD439D59CC4 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: 5C7B76DC93EF45FD9231522EB2CE7B0A Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 42007801000001A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732442000D0200000004000000020000000042000F010000006842005A05000000040000000800000000420090080000000801F76942FF5A7A8A42007C050000000400000000000000004200790100000030420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042000F01000000D842005A05000000040000000A0000000042009008000000083192EDD439D59CC442007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042008C010000005842003E010000005042004005000000040000000100000000420043010000001842004108000000105C7B76DC93EF45FD9231522EB2CE7B0A4200260500000004000000030000000042002802000000040000008000000000 |
| 3 | Client B: Get attribute list In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000C (Get Attribute List) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000C000000004200760100000030420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000 Out: uuidKey, attributes={ * } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07325 (Mon Sep 28 10:26:13 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000C (Get Attribute List) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Digest Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Initial Date Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Unique Identifier Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Last Changed Date 42007801000001D042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732542000D0200000004000000010000000042000F010000017842005A05000000040000000C0000000042007C050000000400000000000000004200790100000150420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042000A070000001443727970746F67726170686963204C656E6774680000000042000A070000001743727970746F6772617068696320416C676F726974686D0042000A0700000005537461746500000042000A0700000006446967657374000042000A070000000C496E697469616C20446174650000000042000A0700000011556E69717565204964656E7469666965720000000000000042000A07000000044E616D650000000042000A070000001843727970746F67726170686963205573616765204D61736B42000A070000000B4F626A6563742054797065000000000042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000A07000000114C617374204368616E676564204461746500000000000000 |
| 4 | Client B: Get attributes In: uuidKey, attributeNames={‘Name’, ‘ContactInformation’} Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information 42007501000000C042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000007842005A05000000040000000B000000004200760100000060420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042000A07000000044E616D650000000042000A0700000013436F6E7461637420496E666F726D6174696F6E0000000000 Out: uuidKey, attributes={ Name={ Name=‘Key1’, NameType=’00000001’ }, ContactInformation=‘Foo’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07325 (Mon Sep 28 10:26:13 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Contact Information Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Foo 420078010000012842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732542000D0200000004000000010000000042000F01000000D042005A05000000040000000B0000000042007C0500000004000000000000000042007901000000A8420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A0700000013436F6E7461637420496E666F726D6174696F6E000000000042000B0700000003466F6F0000000000 |
| 5 | Client B: Add attribute [batch] In: uuidKey, attribute={ x-attribute1=‘Value1’} In: uuidKey, attribute={ x-attribute2=‘Value2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 290C75CAE59F3908 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: BF48C307C95CC22E Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value2 420075010000016042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000008842005A05000000040000000D000000004200900800000008290C75CAE59F39084200760100000060420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000002842000A070000000C782D617474726962757465310000000042000B070000000656616C756531000042000F010000008842005A05000000040000000D000000004200900800000008BF48C307C95CC22E4200760100000060420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000002842000A070000000C782D617474726962757465320000000042000B070000000656616C7565320000 Out: uuidKey, attribute={ x-attribute1=‘Value1’} Out: uuidKey, attribute={ x-attribute2=‘Value2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07326 (Mon Sep 28 10:26:14 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 290C75CAE59F3908 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: BF48C307C95CC22E Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value2 420078010000019042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732642000D0200000004000000020000000042000F010000009842005A05000000040000000D000000004200900800000008290C75CAE59F390842007C050000000400000000000000004200790100000060420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000002842000A070000000C782D617474726962757465310000000042000B070000000656616C756531000042000F010000009842005A05000000040000000D000000004200900800000008BF48C307C95CC22E42007C050000000400000000000000004200790100000060420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000002842000A070000000C782D617474726962757465320000000042000B070000000656616C7565320000 |
| 6 | Client B: Modify attribute [batch] In: uuidKey, attribute={ x-attribute1=‘ModifiedValue1’ } In: uuidKey, attribute={ x-attribute2=‘ModifiedValue2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 42C6D3ED5BFE4F34 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: A391110F7716FCFD Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 420075010000017042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000009042005A05000000040000000E00000000420090080000000842C6D3ED5BFE4F344200760100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F010000009042005A05000000040000000E000000004200900800000008A391110F7716FCFD4200760100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 Out: uuidKey, attribute={ x-ttribute1=‘ModifiedValue1’ } Out: uuidKey, attribute={ x-attribute2=’ModifiedValue2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07326 (Mon Sep 28 10:26:14 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 42C6D3ED5BFE4F34 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: A391110F7716FCFD Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 42007801000001A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732642000D0200000004000000020000000042000F01000000A042005A05000000040000000E00000000420090080000000842C6D3ED5BFE4F3442007C050000000400000000000000004200790100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F01000000A042005A05000000040000000E000000004200900800000008A391110F7716FCFD42007C050000000400000000000000004200790100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 |
| 7 | Client B: Delete attribute [batch] In: uuidKey, attributeNames={‘x-attribute1’} In: uuidKey, attributeNames={‘x-attribute2’} Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: FB10B7D6A5F8F02F Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3B5C2DE222A01A87 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 420075010000013042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000007042005A05000000040000000F000000004200900800000008FB10B7D6A5F8F02F4200760100000048420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042000A070000000C782D617474726962757465310000000042000F010000007042005A05000000040000000F0000000042009008000000083B5C2DE222A01A874200760100000048420091070000002437666261303834392D613363322D346438632D383164642D3961313939393437653437640000000042000A070000000C782D6174747269627574653200000000 Out: uuidKey, attributeNames={‘x-attribute1’} Out: uuidKey, attributeNames={‘x-attribute2’} Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07327 (Mon Sep 28 10:26:15 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: FB10B7D6A5F8F02F Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3B5C2DE222A01A87 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 42007801000001A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732742000D0200000004000000020000000042000F01000000A042005A05000000040000000F000000004200900800000008FB10B7D6A5F8F02F42007C050000000400000000000000004200790100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F01000000A042005A05000000040000000F0000000042009008000000083B5C2DE222A01A8742007C050000000400000000000000004200790100000068420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 |
| 8 | Client A: Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07327 (Mon Sep 28 10:26:15 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732742000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000 |
| 9 | Client A: Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 7fba0849-a3c2-4d8c-81dd-9a199947e47d 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002437666261303834392D613363322D346438632D383164642D39613139393934376534376400000000 Out: Operation Failed, Item Not Found Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07327 (Mon Sep 28 10:26:15 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000001 (Failed) Tag: Result Reason (0x42007B), Type: Enumeration (0x05), Data: 0x00000001 (Item Not Found) Tag: Result Message (0x42007A), Type: Text String (0x07), Data: No Cryptographic Object found with given Unique Identifier 42007801000000D042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732742000D0200000004000000010000000042000F010000007842005A05000000040000000A0000000042007C0500000004000000010000000042007B0500000004000000010000000042007A070000003A4E6F2043727970746F67726170686963204F626A65637420666F756E64207769746820676976656E20556E69717565204964656E746966696572000000000000 |
| 10 | Client A: Destroy (template) In: uuidTemplate Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8383198b-4600-4388-955f-2802cc699e9c 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002438333833313938622D343630302D343338382D393535662D32383032636336393965396300000000 Out: uuidTemplate Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07327 (Mon Sep 28 10:26:15 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8383198b-4600-4388-955f-2802cc699e9c 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732742000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002438333833313938622D343630302D343338382D393535662D32383032636336393965396300000000 |
| 11 | Client A: Get (template) In: uuidTemplate Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8383198b-4600-4388-955f-2802cc699e9c 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002438333833313938622D343630302D343338382D393535662D32383032636336393965396300000000 Out: Operation Failed, Item Not Found Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07327 (Mon Sep 28 10:26:15 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000001 (Failed) Tag: Result Reason (0x42007B), Type: Enumeration (0x05), Data: 0x00000001 (Item Not Found) Tag: Result Message (0x42007A), Type: Text String (0x07), Data: No Cryptographic Object found with given Unique Identifier 42007801000000D042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0732742000D0200000004000000010000000042000F010000007842005A05000000040000000A0000000042007C0500000004000000010000000042007B0500000004000000010000000042007A070000003A4E6F2043727970746F67726170686963204F626A65637420666F756E64207769746820676976656E20556E69717565204964656E746966696572000000000000 |

## Use-case: Asynchronous Locate

This use-case tests the asynchronous capabilities of KMIP using the Locate operation. A key is created and then a Locate request is sent containing the Name of the created key and with the message header Asynchronous Indicator-field set to True. If the server returns an asynchronous response to the Locate, the client then polls the server until the operation is ready. If the server responded asynchronously, a subsequent Locate operation that is also handled asynchronously is then Cancelled, before the key is finally destroyed.

This use-case shows the use of two clients with the same assumptions as in the use-case described in Section 3.1.4 Since the client is unable force the server to respond asynchronously, it is possible for a server to respond synchronously to the requests issued at times 1 and 4, in which case the expected response are the ones shown at times 2 and 5, respectively. In the case of the server not responding asynchronously to the Locate requests, the client is permitted to skip the requests illustrated at time 7 and 8.

| Time | Client A |
| --- | --- |
| 0 | Client A: Create (symmetric key) In: objectType = ‘00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, Name={ NameValue=‘Key1’, NameType=’00000001’ }, CryptographicUsageMask=‘00000004’, ObjectGroup=‘Group1’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000004 (Encrypt) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Group Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Group1 420075010000019042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000014842005A0500000004000000010000000042007601000001304200550500000004000000020000000042008E0100000118420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000400000000420008010000002842000A070000000C4F626A6563742047726F75700000000042000B070000000647726F7570310000 Out: objectType = ‘00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781B (Mon Sep 28 10:47:23 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781B42000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 |
| 1 | Client B: Locate (symmetric key by name) In: asynchronousIndicator=’TRUE’, attributes={ objectType = ‘00000002’, Name={ Name=‘Key1’, NameType=’00000001’} } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Asynchronous Indicator (0x420007), Type: Boolean (0x06), Data: TRUE Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000E04200740100000048420067010000002042006802000000040000000100000000420069020000000400000000000000004200070600000008000000000000000142000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: asyncCorrValue1 Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781C (Mon Sep 28 10:47:24 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000002 (Pending) Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: D1DE142AC6367B4B 420078010000008842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781C42000D0200000004000000010000000042000F010000003042005A0500000004000000080000000042007C050000000400000002000000004200060800000008D1DE142AC6367B4B |
| 2 | Client B: Poll* In: asyncCorrValue1 Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000001A (Poll) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: D1DE142AC6367B4B 420075010000007042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000002842005A05000000040000001A0000000042007601000000104200060800000008D1DE142AC6367B4B Out: uuidKey1 Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781C (Mon Sep 28 10:47:24 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781C42000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 |
| 3 | Client B: Get (symmetric key) In: uuidKey1 Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 Out: objectType = ‘00000002’, uuidKey1, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781D (Mon Sep 28 10:47:25 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: A1DF7B733D8DF7056623FE2D880EF62C Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781D42000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002438623936313231312D393763372D343061362D383636342D6564333334393164616235630000000042008C010000005842003E01000000504200400500000004000000010000000042004301000000184200410800000010A1DF7B733D8DF7056623FE2D880EF62C4200260500000004000000030000000042002802000000040000008000000000 |
| 4 | Client B: Locate (symmetric key by group) In: asynchronousIndicator=’TRUE’, attributes={ objectType = ‘00000002’, ObjectGroup=‘Group1’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Asynchronous Indicator (0x420007), Type: Boolean (0x06), Data: TRUE Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Group Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Group1 42007501000000D04200740100000048420067010000002042006802000000040000000100000000420069020000000400000000000000004200070600000008000000000000000142000D0200000004000000010000000042000F010000007842005A050000000400000008000000004200760100000060420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000002842000A070000000C4F626A6563742047726F75700000000042000B070000000647726F7570310000 Out: asyncCorrValue2 Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781D (Mon Sep 28 10:47:25 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000002 (Pending) Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: 2DCF4F694617FC30 420078010000008842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781D42000D0200000004000000010000000042000F010000003042005A0500000004000000080000000042007C0500000004000000020000000042000608000000082DCF4F694617FC30 |
| 5 | Client B: Poll* In: asyncCorrValue2 Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000001A (Poll) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: 2DCF4F694617FC30 420075010000007042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000002842005A05000000040000001A00000000420076010000001042000608000000082DCF4F694617FC30 Out: uuidKey2 Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781D (Mon Sep 28 10:47:25 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781D42000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 |
| 6 | Client B: Get (symmetric key) In: uuidKey2 Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 Out: objectType = ‘00000002’, uuidKey2, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781D (Mon Sep 28 10:47:25 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: A1DF7B733D8DF7056623FE2D880EF62C Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781D42000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002438623936313231312D393763372D343061362D383636342D6564333334393164616235630000000042008C010000005842003E01000000504200400500000004000000010000000042004301000000184200410800000010A1DF7B733D8DF7056623FE2D880EF62C4200260500000004000000030000000042002802000000040000008000000000 |
| 7 | Client B: Locate (symmetric key by name) In: asynchronousIndicator=’TRUE’, attributes={ objectType = ‘00000002’, Name= { Name=‘Key1’, NameType=’00000001’ } } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Asynchronous Indicator (0x420007), Type: Boolean (0x06), Data: TRUE Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000E04200740100000048420067010000002042006802000000040000000100000000420069020000000400000000000000004200070600000008000000000000000142000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: asyncCorrValue5 Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781E (Mon Sep 28 10:47:26 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000002 (Pending) Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: D48BDD01A8FFEC80 420078010000008842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781E42000D0200000004000000010000000042000F010000003042005A0500000004000000080000000042007C050000000400000002000000004200060800000008D48BDD01A8FFEC80 |
| 8 | Client B: Cancel In: asyncCorrValue5 Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000019 (Cancel) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: D48BDD01A8FFEC80 420075010000007042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000002842005A0500000004000000190000000042007601000000104200060800000008D48BDD01A8FFEC80 Out: asyncCorrValue5, CancelResult=’00000001’ Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781F (Mon Sep 28 10:47:27 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000019 (Cancel) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Asynchronous Correlation Value (0x420006), Type: Octet String (0x08), Data: D48BDD01A8FFEC80 Tag: Cancellation Result (0x420012), Type: Enumeration (0x05), Data: 0x00000001 (Cancelled) 42007801000000A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781F42000D0200000004000000010000000042000F010000004842005A0500000004000000190000000042007C0500000004000000000000000042007901000000204200060800000008D48BDD01A8FFEC8042001205000000040000000100000000 |
| 9 | Client A: Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781F (Mon Sep 28 10:47:27 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 8b961211-97c7-40a6-8664-ed33491dab5c 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781F42000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002438623936313231312D393763372D343061362D383636342D65643333343931646162356300000000 |

* = executed until response is ready

# Key life cycle support

## Use-case: Revoke scenario

This use-case tests the revocation aspect of the key life cycle support in KMIP. A key is created and a Get Attribute for the State-attribute reveals that the key is in Pre-active state. The Activation Date is then set, which changes the state to Active. The key is then revoked with a revocation reason of Compromised and the state subsequently changed to Compromised, but this does not stop a client from being able to add, modify and delete attributes or even get the key (since we assume here that the out-of-band registration has been used to make the server aware of the fact that the client is capable of interpreting the attributes of the key and determining what it is allowed to do with the key). To clean up, the created key is finally destroyed.

| Time | Client A |
| --- | --- |
| 0 | Client A: Create (symmetric key) In: objectType = ‘00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, Name={ NameValue=‘Key1’, NameType=’00000001’ }, CryptographicUsageMask=‘00000004’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000004 (Encrypt) 420075010000016042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000011842005A0500000004000000010000000042007601000001004200550500000004000000020000000042008E01000000E8420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000400000000 Out: objectType = ‘00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0781F (Mon Sep 28 10:47:27 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0781F42000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 |
| 1 | Client A: Get attribute In: uuidKey, attributeName={‘State’} Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A05000000040000000B000000004200760100000040420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A07000000055374617465000000 Out: uuidKey, attribute={ State=‘00000001’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07820 (Mon Sep 28 10:47:28 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000001 (Pre-Active) 42007801000000D842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782042000D0200000004000000010000000042000F010000008042005A05000000040000000B0000000042007C050000000400000000000000004200790100000058420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002042000A0700000005537461746500000042000B05000000040000000100000000 |
| 2 | Client A: Add attribute In: uuidKey, attribute={ ActivationDate=’2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Activation Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x0000000000000002 (Thu Jan 01 01:00:02 CET 1970) 42007501000000C042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000007842005A05000000040000000D000000004200760100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000F41637469766174696F6E20446174650042000B09000000080000000000000002 Out: uuidKey, attribute={ ActivationDate=’2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07820 (Mon Sep 28 10:47:28 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Activation Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x0000000000000002 (Thu Jan 01 01:00:02 CET 1970) 42007801000000E042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782042000D0200000004000000010000000042000F010000008842005A05000000040000000D0000000042007C050000000400000000000000004200790100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000F41637469766174696F6E20446174650042000B09000000080000000000000002 |
| 3 | Client A: Get attribute In: uuidKey, attributeName={ ‘State’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A05000000040000000B000000004200760100000040420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A07000000055374617465000000 Out: uuidKey, attribute={ State=‘00000002’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07820 (Mon Sep 28 10:47:28 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Active) 42007801000000D842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782042000D0200000004000000010000000042000F010000008042005A05000000040000000B0000000042007C050000000400000000000000004200790100000058420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002042000A0700000005537461746500000042000B05000000040000000200000000 |
| 4 | Client B: Locate (symmetric key by name) In: objectType = ‘00000002’, attributes={ Name={ Name=‘Key1’, NameType=’00000001’ } } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000D042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07821 (Mon Sep 28 10:47:29 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782142000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 |
| 5 | Client B: Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 Out: objectType = ‘00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07821 (Mon Sep 28 10:47:29 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: E6C15B28BB6C7A268E9ADEA471A36F23 Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782142000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042008C010000005842003E01000000504200400500000004000000010000000042004301000000184200410800000010E6C15B28BB6C7A268E9ADEA471A36F234200260500000004000000030000000042002802000000040000008000000000 |
| 6 | Client B: Revoke (symmetric key as compromised) In: uuidKey, RevocationReason=’00000002’, CompromiseOccurrenceTime=’6’ Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000013 (Revoke) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Revocation Reason (0x42007E), Type: Structure (0x01), Data: Tag: Revocation Reason Code (0x42007F), Type: Enumeration (0x05), Data: 0x00000002 (Key Compromise) Tag: Compromise Occurrence Date (0x42001F), Type: Date-Time (0x09), Data: 0x0000000000000006 (Thu Jan 01 01:00:06 CET 1970) 42007501000000B842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000007042005A050000000400000013000000004200760100000058420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042007E010000001042007F0500000004000000020000000042001F09000000080000000000000006 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07822 (Mon Sep 28 10:47:30 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000013 (Revoke) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782242000D0200000004000000010000000042000F010000005842005A0500000004000000130000000042007C050000000400000000000000004200790100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 |
| 7 | Client B: Get attribute In: uuidKey, attributeName={ ‘State’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A05000000040000000B000000004200760100000040420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A07000000055374617465000000 Out: uuidKey, attribute={ State=‘00000004’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07822 (Mon Sep 28 10:47:30 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000004 (Compromised) 42007801000000D842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782242000D0200000004000000010000000042000F010000008042005A05000000040000000B0000000042007C050000000400000000000000004200790100000058420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002042000A0700000005537461746500000042000B05000000040000000400000000 |
| 8 | Client A: Get attribute list In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000C (Get Attribute List) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000C000000004200760100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 Out: uuidKey, attributes = { * } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07822 (Mon Sep 28 10:47:30 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000C (Get Attribute List) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Compromise Occurrence Date Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Compromise Date Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Digest Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Initial Date Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Activation Date Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Revocation Reason Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Unique Identifier Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Last Changed Date 420078010000022842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782242000D0200000004000000010000000042000F01000001D042005A05000000040000000C0000000042007C0500000004000000000000000042007901000001A8420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A070000001443727970746F67726170686963204C656E6774680000000042000A070000001743727970746F6772617068696320416C676F726974686D0042000A0700000005537461746500000042000A070000001A436F6D70726F6D697365204F6363757272656E6365204461746500000000000042000A070000000F436F6D70726F6D69736520446174650042000A0700000006446967657374000042000A070000000C496E697469616C20446174650000000042000A070000000F41637469766174696F6E20446174650042000A07000000115265766F636174696F6E20526561736F6E0000000000000042000A0700000011556E69717565204964656E7469666965720000000000000042000A07000000044E616D650000000042000A070000001843727970746F67726170686963205573616765204D61736B42000A070000000B4F626A6563742054797065000000000042000A07000000114C617374204368616E676564204461746500000000000000 |
| 9 | Client A: Get attributes In: uuidKey, attributeName = { ‘State’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A05000000040000000B000000004200760100000040420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A07000000055374617465000000 Out: uuidKey, attribute={ State=‘00000004’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07822 (Mon Sep 28 10:47:30 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000B (Get Attributes) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: State Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000004 (Compromised) 42007801000000D842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782242000D0200000004000000010000000042000F010000008042005A05000000040000000B0000000042007C050000000400000000000000004200790100000058420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002042000A0700000005537461746500000042000B05000000040000000400000000 |
| 10 | Client A: Add attribute [batch] In: uuidKey, attribute={ x-attribute1=‘Value1’ } In: uuidKey, attribute={ x-attribute2=’Value2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 5CD7C98FC5B52FF7 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: F0CB35D89BB9D251 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value2 420075010000016042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000008842005A05000000040000000D0000000042009008000000085CD7C98FC5B52FF74200760100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000C782D617474726962757465310000000042000B070000000656616C756531000042000F010000008842005A05000000040000000D000000004200900800000008F0CB35D89BB9D2514200760100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000C782D617474726962757465320000000042000B070000000656616C7565320000 Out: uuidKey, attribute={ x-attribute1=‘Value1’ } Out: uuidKey, attribute={ x-attribute2=‘Value2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07823 (Mon Sep 28 10:47:31 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 5CD7C98FC5B52FF7 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: F0CB35D89BB9D251 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: Value2 420078010000019042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782342000D0200000004000000020000000042000F010000009842005A05000000040000000D0000000042009008000000085CD7C98FC5B52FF742007C050000000400000000000000004200790100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000C782D617474726962757465310000000042000B070000000656616C756531000042000F010000009842005A05000000040000000D000000004200900800000008F0CB35D89BB9D25142007C050000000400000000000000004200790100000060420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000002842000A070000000C782D617474726962757465320000000042000B070000000656616C7565320000 |
| 11 | Client A: Modify attribute [batch] In: uuidKey, attribute={ x-attribute1=‘ModifiedValue1’ } In: uuidKey, attribute={ x-attribute2=’ModifiedValue2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: C06597C23C952144 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3D9CF6E0445252B8 Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 420075010000017042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000009042005A05000000040000000E000000004200900800000008C06597C23C9521444200760100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F010000009042005A05000000040000000E0000000042009008000000083D9CF6E0445252B84200760100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 Out: uuidKey, attribute={ x-attribute1=‘ModifiedValue1’ } Out: uuidKey, attribute={ x-attribute2=‘ModifiedValue2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07823 (Mon Sep 28 10:47:31 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: C06597C23C952144 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 3D9CF6E0445252B8 Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 42007801000001A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782342000D0200000004000000020000000042000F01000000A042005A05000000040000000E000000004200900800000008C06597C23C95214442007C050000000400000000000000004200790100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F01000000A042005A05000000040000000E0000000042009008000000083D9CF6E0445252B842007C050000000400000000000000004200790100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 |
| 12 | Client A: Delete attribute [batch] In: uuidKey, attributeNames={ ‘x-attribute1’ } In: uuidKey, attributeNames={ ‘x-attribute2’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 1A1B48172DF57ABC Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: B77FD0753B7C95ED Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 420075010000013042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000007042005A05000000040000000F0000000042009008000000081A1B48172DF57ABC4200760100000048420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A070000000C782D617474726962757465310000000042000F010000007042005A05000000040000000F000000004200900800000008B77FD0753B7C95ED4200760100000048420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042000A070000000C782D6174747269627574653200000000 Out: uuidKey, attributeNames={ ‘x-attribute1’ } Out: uuidKey, attributeNames={ ‘x-attribute2’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07826 (Mon Sep 28 10:47:34 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: 1A1B48172DF57ABC Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute1 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue1 Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000F (Delete Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: B77FD0753B7C95ED Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-attribute2 Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: ModifiedValue2 42007801000001A042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782642000D0200000004000000020000000042000F01000000A042005A05000000040000000F0000000042009008000000081A1B48172DF57ABC42007C050000000400000000000000004200790100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465310000000042000B070000000E4D6F64696669656456616C756531000042000F01000000A042005A05000000040000000F000000004200900800000008B77FD0753B7C95ED42007C050000000400000000000000004200790100000068420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000420008010000003042000A070000000C782D617474726962757465320000000042000B070000000E4D6F64696669656456616C7565320000 |
| 13 | Client A: Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 Out: objectType = ‘00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07827 (Mon Sep 28 10:47:35 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: E6C15B28BB6C7A268E9ADEA471A36F23 Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782742000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002433333364633962392D386537332D346666362D613337622D3432333639663561343236320000000042008C010000005842003E01000000504200400500000004000000010000000042004301000000184200410800000010E6C15B28BB6C7A268E9ADEA471A36F234200260500000004000000030000000042002802000000040000008000000000 |
| 14 | Client A: Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07827 (Mon Sep 28 10:47:35 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 333dc9b9-8e73-4ff6-a37b-42369f5a4262 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782742000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002433333364633962392D386537332D346666362D613337622D34323336396635613432363200000000 |

# Auditing and reporting

## Use-case: Get usage allocation scenario

This use-case tests the usage management functionality of KMIP. A key is created and the Activation Date and Protect Stop Date attributes are set in such a way as to allow the Get Usage Allocation operation to be performed. The value of the Usage Limits attribute is set to 1000 bytes, and two subsequent requests for 500 bytes succeed, while a third fails since the usage allocation has been used up. The key is finally destroyed. This use-case shows the use of multiple clients with the assumptions regarding the clients being the same as in the use-case described in Section 3.1.4

| Time | Client A |
| --- | --- |
| 0 | Client A: Create (symmetric key) In: objectType = ‘00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, NameValue={ Name=‘Key1’, NameType=’00000001’ }, CryptographicUsageMask=‘00000004’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Algorithm Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Length Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000080 (128) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000004 (Encrypt) 420075010000016042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000011842005A0500000004000000010000000042007601000001004200550500000004000000020000000042008E01000000E8420008010000003042000A070000001743727970746F6772617068696320416C676F726974686D0042000B05000000040000000300000000420008010000003042000A070000001443727970746F67726170686963204C656E6774680000000042000B02000000040000008000000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B02000000040000000400000000 Out: objectType = ‘00000002’, uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07828 (Mon Sep 28 10:47:36 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000001 (Create) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000C042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782842000D0200000004000000010000000042000F010000006842005A0500000004000000010000000042007C05000000040000000000000000420079010000004042005505000000040000000200000000420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |
| 1 | Client A: Add attribute [batch] In: uuidKey, attribute={ ActivationDate=‘2’ } In: uuidKey, attribute={ ProtectStopDate=’<NOW+10min>’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: E1AE8A5206CC749A Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Activation Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x0000000000000002 (Thu Jan 01 01:00:02 CET 1970) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: C6CAA6E0C409336F Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Protect Stop Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x000000004AC07A80 (Mon Sep 28 10:57:36 CEST 2009) 420075010000016842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000020000000042000F010000008842005A05000000040000000D000000004200900800000008E1AE8A5206CC749A4200760100000060420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000002842000A070000000F41637469766174696F6E20446174650042000B0900000008000000000000000242000F010000009042005A05000000040000000D000000004200900800000008C6CAA6E0C409336F4200760100000068420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000003042000A070000001150726F746563742053746F7020446174650000000000000042000B0900000008000000004AC07A80 Out: uuidKey, attribute={ ActivationDate=’2’ } Out: uuidKey, attribute={ ProtectStopDate=’<NOW+10min>’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC07828 (Mon Sep 28 10:47:36 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000002 (2) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: E1AE8A5206CC749A Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Activation Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x0000000000000002 (Thu Jan 01 01:00:02 CET 1970) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Unique Batch Item ID (0x420090), Type: Octet String (0x08), Data: C6CAA6E0C409336F Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Protect Stop Date Tag: Attribute Value (0x42000B), Type: Date-Time (0x09), Data: 0x000000004AC07A80 (Mon Sep 28 10:57:36 CEST 2009) 420078010000019842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782842000D0200000004000000020000000042000F010000009842005A05000000040000000D000000004200900800000008E1AE8A5206CC749A42007C050000000400000000000000004200790100000060420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000002842000A070000000F41637469766174696F6E20446174650042000B0900000008000000000000000242000F01000000A042005A05000000040000000D000000004200900800000008C6CAA6E0C409336F42007C050000000400000000000000004200790100000068420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000003042000A070000001150726F746563742053746F7020446174650000000000000042000B0900000008000000004AC07A80 |
| 2 | Client A: Add Attribute In: uuidKey, attribute={ UsageLimits={ UsageLimitsTotalBytes=‘1000’} } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Usage Limits Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Usage Limits Total Bytes (0x420095), Type: Big Integer (0x04), Data: 03E8 (1000) 42007501000000C842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008042005A05000000040000000D000000004200760100000068420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000003042000A070000000C5573616765204C696D6974730000000042000B0100000010420095040000000800000000000003E8 Out: uuidKey, attribute={ UsageLimits={ UsageLimitsTotalBytes= ‘1000’, UsageLimitsByteCount=‘1000’} } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782A (Mon Sep 28 10:47:38 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Usage Limits Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Usage Limits Total Bytes (0x420095), Type: Big Integer (0x04), Data: 00000000000003E8 (1000) Tag: Usage Limits Byte Count (0x420093), Type: Big Integer (0x04), Data: 00000000000003E8 (1000) 42007801000000F842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782A42000D0200000004000000010000000042000F01000000A042005A05000000040000000D0000000042007C050000000400000000000000004200790100000078420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420008010000004042000A070000000C5573616765204C696D6974730000000042000B0100000020420095040000000800000000000003E8420093040000000800000000000003E8 |
| 3 | Client B: Locate (symmetric key by name) In: objectType = ‘00000002’, attributes={ Name={ Name=‘Key1’, NameType= ‘00000001’} } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000D042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782A (Mon Sep 28 10:47:38 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782A42000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |
| 4 | Client B: Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 Out: objectType = ‘00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782A (Mon Sep 28 10:47:38 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: 3D41DF1C5C20E272212D86D762A8C7D4 Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782A42000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002434666563336135392D623231372D346162662D383461642D6166313534373032343631350000000042008C010000005842003E010000005042004005000000040000000100000000420043010000001842004108000000103D41DF1C5C20E272212D86D762A8C7D44200260500000004000000030000000042002802000000040000008000000000 |
| 5 | Client B: Get usage allocation In: uuidKey, UsageLimitsByteCount=’500’ Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Usage Limits Byte Count (0x420093), Type: Big Integer (0x04), Data: 01F4 (500) 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A050000000400000011000000004200760100000040420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420093040000000800000000000001F4 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782A (Mon Sep 28 10:47:38 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782A42000D0200000004000000010000000042000F010000005842005A0500000004000000110000000042007C050000000400000000000000004200790100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |
| 6 | Client A: Get usage allocation In: uuidKey, UsageLimitsByteCount=’500’ Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Usage Limits Byte Count (0x420093), Type: Big Integer (0x04), Data: 01F4 (500) 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A050000000400000011000000004200760100000040420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420093040000000800000000000001F4 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782B (Mon Sep 28 10:47:39 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782B42000D0200000004000000010000000042000F010000005842005A0500000004000000110000000042007C050000000400000000000000004200790100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |
| 7 | Client C: Locate (symmetric key by name) In: objectType = ‘00000002’, attributes={ Name={ Name=‘Key1’, NameType=‘00000001’} } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Object Type Tag: Attribute Value (0x42000B), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Name Tag: Attribute Value (0x42000B), Type: Structure (0x01), Data: Tag: Name Value (0x420053), Type: Text String (0x07), Data: Key1 Tag: Name Type (0x420052), Type: Enumeration (0x05), Data: 0x00000001 (Uninterpreted text string) 42007501000000D042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008842005A050000000400000008000000004200760100000070420008010000002842000A070000000B4F626A6563742054797065000000000042000B05000000040000000200000000420008010000003842000A07000000044E616D650000000042000B010000002042005307000000044B6579310000000042005205000000040000000100000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782B (Mon Sep 28 10:47:39 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000008 (Locate) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782B42000D0200000004000000010000000042000F010000005842005A0500000004000000080000000042007C050000000400000000000000004200790100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |
| 8 | Client C: Get (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A05000000040000000A000000004200760100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 Out: objectType = ‘00000002’, uuidKey, symmetricKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782B (Mon Sep 28 10:47:39 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000A (Get) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: 3D41DF1C5C20E272212D86D762A8C7D4 Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420078010000012042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782B42000D0200000004000000010000000042000F01000000C842005A05000000040000000A0000000042007C0500000004000000000000000042007901000000A042005505000000040000000200000000420091070000002434666563336135392D623231372D346162662D383461642D6166313534373032343631350000000042008C010000005842003E010000005042004005000000040000000100000000420043010000001842004108000000103D41DF1C5C20E272212D86D762A8C7D44200260500000004000000030000000042002802000000040000008000000000 |
| 9 | Client C: Get usage allocation In: uuidKey, UsageLimitsByteCount=’500’ Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 Tag: Usage Limits Byte Count (0x420093), Type: Big Integer (0x04), Data: 01F4 (500) 42007501000000A042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000005842005A050000000400000011000000004200760100000040420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000420093040000000800000000000001F4 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782B (Mon Sep 28 10:47:39 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000011 (Get Usage Allocation) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000001 (Failed) Tag: Result Reason (0x42007B), Type: Enumeration (0x05), Data: 0x0000000C (Permission Denied) Tag: Result Message (0x42007A), Type: Text String (0x07), Data: Unable to allocate requested byte amount 42007801000000B842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782B42000D0200000004000000010000000042000F010000006042005A0500000004000000110000000042007C0500000004000000010000000042007B05000000040000000C0000000042007A0700000028556E61626C6520746F20616C6C6F6361746520726571756573746564206279746520616D6F756E74 |
| 10 | Client A: Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782C (Mon Sep 28 10:47:40 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: 4fec3a59-b217-4abf-84ad-af1547024615 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782C42000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002434666563336135392D623231372D346162662D383461642D61663135343730323436313500000000 |

# Key Interchange, Key Exchange

## Use-case: Import of a Third-party Key

This use-case tests the import of a foreign key using the Register operation. To validate that the registered key is treated the same as a locally created key, an attribute is added to the key and then modified. Finally, the key is destroyed.

| Time | Request/Response messages |
| --- | --- |
| 0 | Register (symmetric key) In: objectType = ‘00000002’, attributes={ CryptographicUsageMask=‘00000004’ }, foreignSymmetricKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Object Type (0x420055), Type: Enumeration (0x05), Data: 0x00000002 (Symmetric Key) Tag: Template-Attribute (0x42008E), Type: Structure (0x01), Data: Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: Cryptographic Usage Mask Tag: Attribute Value (0x42000B), Type: Integer (0x02), Data: 0x00000004 (Encrypt) Tag: Symmetric Key (0x42008C), Type: Structure (0x01), Data: Tag: Key Block (0x42003E), Type: Structure (0x01), Data: Tag: Key Format Type (0x420040), Type: Enumeration (0x05), Data: 0x00000001 Tag: Key Value (0x420043), Type: Structure (0x01), Data: Tag: Key Material (0x420041), Type: Octet String (0x08), Data: 0123456789ABCDEF0123456789ABCDEF Tag: Cryptographic Algorithm (0x420026), Type: Enumeration (0x05), Data: 0x00000003 (AES) Tag: Cryptographic Length (0x420028), Type: Integer (0x02), Data: 0x00000080 (128) 420075010000011042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F01000000C842005A0500000004000000030000000042007601000000B04200550500000004000000020000000042008E0100000038420008010000003042000A070000001843727970746F67726170686963205573616765204D61736B42000B0200000004000000040000000042008C010000005842003E010000005042004005000000040000000100000000420043010000001842004108000000100123456789ABCDEF0123456789ABCDEF4200260500000004000000030000000042002802000000040000008000000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782C (Mon Sep 28 10:47:40 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000003 (Register) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782C42000D0200000004000000010000000042000F010000005842005A0500000004000000030000000042007C050000000400000000000000004200790100000030420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000 |
| 1 | Add attribute In: uuidKey, attribute={ x-provider=‘unknown’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-provider Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: unknown 42007501000000C042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000007842005A05000000040000000D000000004200760100000060420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000420008010000002842000A070000000A782D70726F766964657200000000000042000B0700000007756E6B6E6F776E00 Out: uuidKey, attribute={ x-provider=‘unknown’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782E (Mon Sep 28 10:47:42 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000D (Add Attribute) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-provider Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: unknown 42007801000000E042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782E42000D0200000004000000010000000042000F010000008842005A05000000040000000D0000000042007C050000000400000000000000004200790100000060420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000420008010000002842000A070000000A782D70726F766964657200000000000042000B0700000007756E6B6E6F776E00 |
| 2 | Modify attribute In: uuidKey, attribute={ x-provider=‘third party’ } Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-provider Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: third party 42007501000000C842007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000008042005A05000000040000000E000000004200760100000068420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000420008010000003042000A070000000A782D70726F766964657200000000000042000B070000000B74686972642070617274790000000000 Out: uuidKey, attribute={ x-provider=‘third party’ } Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782E (Mon Sep 28 10:47:42 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x0000000E (Modify Attribute) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b Tag: Attribute (0x420008), Type: Structure (0x01), Data: Tag: Attribute Name (0x42000A), Type: Text String (0x07), Data: x-provider Tag: Attribute Value (0x42000B), Type: Text String (0x07), Data: third party 42007801000000E842007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782E42000D0200000004000000010000000042000F010000009042005A05000000040000000E0000000042007C050000000400000000000000004200790100000068420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000420008010000003042000A070000000A782D70726F766964657200000000000042000B070000000B74686972642070617274790000000000 |
| 3 | Destroy (symmetric key) In: uuidKey Tag: Request Message (0x420075), Type: Structure (0x01), Data: Tag: Request Header (0x420074), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Request Payload (0x420076), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b 420075010000009042007401000000384200670100000020420068020000000400000001000000004200690200000004000000000000000042000D0200000004000000010000000042000F010000004842005A050000000400000014000000004200760100000030420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000 Out: uuidKey Tag: Response Message (0x420078), Type: Structure (0x01), Data: Tag: Response Header (0x420077), Type: Structure (0x01), Data: Tag: Protocol Version (0x420067), Type: Structure (0x01), Data: Tag: Protocol Version Major (0x420068), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Protocol Version Minor (0x420069), Type: Integer (0x02), Data: 0x00000000 (0) Tag: Time Stamp (0x42008F), Type: Date-Time (0x09), Data: 0x000000004AC0782E (Mon Sep 28 10:47:42 CEST 2009) Tag: Batch Count (0x42000D), Type: Integer (0x02), Data: 0x00000001 (1) Tag: Batch Item (0x42000F), Type: Structure (0x01), Data: Tag: Operation (0x42005A), Type: Enumeration (0x05), Data: 0x00000014 (Destroy) Tag: Result Status (0x42007C), Type: Enumeration (0x05), Data: 0x00000000 (Success) Tag: Response Payload (0x420079), Type: Structure (0x01), Data: Tag: Unique Identifier (0x420091), Type: Text String (0x07), Data: bb806453-5c75-42c2-80bd-4e52f1ceb57b 42007801000000B042007701000000484200670100000020420068020000000400000001000000004200690200000004000000000000000042008F0900000008000000004AC0782E42000D0200000004000000010000000042000F010000005842005A0500000004000000140000000042007C050000000400000000000000004200790100000030420091070000002462623830363435332D356337352D343263322D383062642D34653532663163656235376200000000 |

# Vendor Extensions

These use-cases test the handling of unknown message extensions with vendor-specific content.

## Use-case: Unrecognized Message Extension with Criticality Indicator false

A create request is issued and the request contains a Message Extension with the Criticality Indicator set to false. The server does not understand the extension, but since it is non-critical, the create request is processed normally. Subsequently, the created key is deleted.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’ }, MessageExtension={ VendorIdentification=’Acme’, CriticalityIndicator=’false’, VendorExtension={ tag=’0x540001’, type=’text string’, value=’na’ } } Out: objectType=’00000002’, uuidKey |
| 1 | Destroy (symmetric key) In: uuidKey Out: uuidKey |

## Use-case: Unrecognized Message Extension with Criticality Indicator true

A create request is issued and the request contains a Message Extension with the Criticality Indicator set to true. The server does not understand the extension, and since it is critical, the create request fails and an error is returned.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’ }, MessageExtension={ VendorIdentification=’Acme’, CriticalityIndicator=’true’, VendorExtension={ tag=’0x540001’, type=’text string’, value=’na’ } } Out: Operation Failed, Feature Not Supported |

# Asymmetric keys

Creation of keys using “Create Key Pair” operation, locating pair using Link attribute.

## Use-case: Create a Key Pair

Create a new private/public key pair. Make sure they are linked correctly by issuing Locate commands with the assigned Unique Identifiers. Finally delete both key halves.

| Time | Client A |
| --- | --- |
| 0 | Create Key Pair In: commonAttributes={ CryptographicAlgorithm=’RSA’, CryptographicLength=’1024’, CryptographicUsageMask=‘0000000C’ }, privateKeyAttributes={ Name={ NameValue=‘PrivateKey1’, NameType=’00000001’ } }, publicKeyAttributes={ NameValue=‘PublicKey1’, NameType=’00000001’ } } Out: uuidPrivateKey, uuidPublicKey |
| 1 | Locate (Public Key) In: attributes={ objectType=’PublicKey’, Link={ LinkType=‘PrivateKeyLink’, LinkedObjectIdentifier=uuidPrivateKey } } Out: uuidPublicKey |
| 2 | Locate (Private Key) In: attributes={ objectType=’PrivateKey’, Link={ LinkType=‘PublicKeyLink’, LinkedObjectIdentifier=uuidPublicKey } } Out: uuidPrivateKey |
| 3 | Destroy In: uuidPrivateKey Out: uuidPrivateKey |
| 4 | Destroy In: uuidPublicKey Out: uuidPublicKey |

## Use-case: Register Both Halves of a Key Pair

Register a private key and a public key and set the Link attribute to point to each other. Verify the links were set correctly by locating the keys based on the link attributes, and then delete both objects.

| Time | Client A |
| --- | --- |
| 0 | Register (Private Key) In: objectType=’00000004’, attributes={ CryptographicUsageMask=‘0000000C’ }, foreignPrivateKey Out: uuidPrivateKey |
| 1 | Register (Public Key) In: objectType=’00000004’, attributes={ CryptographicUsageMask=‘0000000C’, Link={ LinkType=‘PrivateKeyLink’, LinkedObjectIdentifier=uuidPrivateKey } }, foreignPublicKey Out: uuidPublicKey |
| 2 | Add attribute In: uuidPrivateKey, attribute={ Link={ LinkType=‘PublicKeyLink’, LinkedObjectIdentifier=uuidPublicKey } } Out: uuidPrivateKey, attribute={ Link={ LinkType=‘PublicKeyLink’, LinkedObjectIdentifier=uuidPublicKey } } |
| 3 | Locate (Public Key) In: attributes={ objectType=’PublicKey’, Link={ LinkType=‘PrivateKeyLink’, LinkedObjectIdentifier=uuidPrivateKey } } Out: uuidPublicKey |
| 4 | Locate (Private Key) In: attributes={ objectType=’PrivateKey’, Link={ LinkType=‘PublicKeyLink’, LinkedObjectIdentifier=uuidPublicKey } } Out: uuidPrivateKey |
| 5 | Destroy In: uuidPrivateKey Out: uuidPrivateKey |
| 6 | Destroy In: uuidPublicKey Out: uuidPublicKey |

# Key Roll-over

These use-cases test manual key roll-over using the “Re-key” operation. In particular, they test the formatting of the Re-key command, the handling and server-side processing of the various Time attributes and the setting of some other attributes that are not automatically copied from the existing key to the new key.

## Use-case: Create a Key, Re-key

Create a symmetric key with a specific name, and then use Locate to find the key. After using Re-key to create a new key, verify that the name was removed from the existing key and copied to the new key. Also verify that the key material for the old key is still retrievable. To clean up, both keys are deleted.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’, Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: objectType=’00000002’, uuidKey |
| 1 | Locate In: attributes={ Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: uuidKey |
| 2 | Rekey In: uuidKey Out: uuidNewKey |
| 3 | Locate In: attributes={ Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: uuidNewKey |
| 4 | Get Attribute In: uuidKey, attributeName={‘Name’} Out: Operation Failed, Item Not Found |
| 5 | Get (symmetric key) In: uuidKey Out: objectType = ‘00000002’, uuidKey, symmetricKey |
| 6 | Destroy In: uuidKey Out: uuidKey |
| 7 | Destroy In: uuidNewKey Out: uuidNewKey |

## Use-case: Existing Key Expired, Re-key with Same lifecycle

Create a new symmetric key with a name. Then add the Activation Date and Deactivation Date attributes based on the timestamp in the response to the Create request. The Activation Date is set to a time in the past and the Deactivation Date to a time in the near future. Repeated Get Attribute calls are performed to verify that the state is first “Active”, then subsequently “Deactive”. Then issue a Re-key request, including an Activation Date attribute with the value set to the previously specified Deactivation Date of the existing key. Verify from the response that the Activation Date and Deactivation Date attributes were set correctly (if they are not returned, issue a Get Attribute request). Do a Get Attribute operation to verify that the state of the new key is “Active”. To clean up, both keys are deleted.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’ } Out: objectType=’00000002’, uuidKey |
| 1 | Add Activation Date, Deactivation Date attributes based on Timestamp in previous response (batch) In: uuidKey, attribute={ ActivationDate=’ <Timestamp in previous response – 365 days>’ } In: uuidKey, attribute={ DeactivationDate=’<Timestamp in previous response + 2 minutes>’ } Out: uuidKey, attribute={ ActivationDate=’ <Timestamp in previous response - 1 year>’ } Out: uuidKey, attribute={ DeactivationDate=’ <Timestamp in previous response + 2 minutes>’ } |
| 2 | Get Attribute * Repeated until state changes to Deactivated In: uuidKey, attributeName={‘State’} Out: uuidKey, attribute={ State=‘Active’ } |
| 3 | Get Attribute In: uuidKey, attributeName={‘State’} Out: uuidKey, attribute={ State=‘Deactive’ } |
| 4 | Rekey In: uuidKey, attribute={ offset=’018B8200’ (300 days)} Out: uuidNewKey |
| 5 | Get Attribute In: uuidNewKey, attributeName={‘ ActivationDate’, ‘DectivationDate’ } Out: uuidNewKey, attribute={ ActivationDate=’ <Value of ActivationTime in existing key + 300 days>’, DectivationDate=’<Value of DeactivationDate of existing key + 300 days>’ } |
| 6 | Get Attribute In: uuidNewKey, attributeName={‘State’} Out: uuidNewKey, attribute={ State=‘Active’ } |
| 7 | Destroy In: uuidKey Out: uuidKey |
| 8 | Destroy In: uuidNewKey Out: uuidNewKey |

## Use-case: Existing Key Compromised, Re-key with same lifecycle

Create a new symmetric key with the Activation Date in the past. Do a Get Attribute operation on the State attribute to verify the key is “Active”. Then revoke the key as compromised, verify that the state has changed to “Compromised”. Create a replacement key using Re-key with the offset set to ‘0’ to indicate that the times are to be copied from the existing key. Do a Get Attribute operation to verify that the state of the new key is “Active”. To clean up, both keys are deleted.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’, Name={ NameValue=‘rekeyKey’, NameType=’00000001’ }, ActivationDate=’2’ } Out: objectType=’00000002’, uuidKey |
| 1 | Get Attribute In: uuidKey, attributeName={‘State’} Out: uuidKey, attribute={ State=‘Active’ } |
| 2 | Revoke (symmetric key as compromised) In: uuidKey, RevocationReason=’00000002’, CompromiseOccurrenceDate=’6’ Out: uuidKey |
| 3 | Get Attribute In: uuidKey, attributeName={‘State’} Out: uuidKey, attribute={ State=‘Compromised’ } |
| 4 | Rekey In: uuidKey, offset=’0’ Out: uuidNewKey |
| 5 | Get Attribute In: uuidNewKey, attributeName={‘State’} Out: uuidNewKey, attribute={ State=‘Active’ } |
| 6 | Destroy In: uuidKey Out: uuidKey |
| 7 | Destroy In: uuidNewKey Out: uuidNewKey |

## Use-case: Create key, Re-key with new lifecycle

Create a symmetric key with a specific name, then use Locate to find the key. After using Re-key to create a new key, verify that the name was removed from the existing key and copied to the new key. To clean up, both keys are deleted.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’, Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: objectType=’00000002’, uuidKey |
| 1 | Locate In: attributes={ Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: uuidKey |
| 2 | Rekey In: uuidKey, attributes={ ActivationDate=’0000000043B7B630’, ProcessStartDate=’0000000043B7B630’, ProtectStopDate=’000000005E0C7BB0’, DeactivationDate=’000000005E0C7BB0’ } Out: uuidNewKey |
| 3 | Get Attribute In: uuidKey, attributeName={‘Name’} Out: Operation Failed, Item Not Found |
| 4 | Get Attribute In: uuidKey, attributeName={ ‘ActivationDate’, ‘ProcessStartDate’, ‘ProtectStopDate’, ‘DeactivationDate’ } Out: uuidKey, attribute={ ActivationDate=’0000000043B7B630’, ProcessStartDate=’0000000043B7B630’, ProtectStopDate=’000000005E0C7BB0’, DeactivationDate=’000000005E0C7BB0’ } |
| 5 | Locate In: attributes={ Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: uuidNewKey |
| 6 | Destroy In: uuidKey Out: uuidKey |
| 7 | Destroy In: uuidNewKey Out: uuidNewKey |

## Use-case: Obtain Lease for Expired Key

Create a symmetric key with a specific name and obtain a lease. Revoke the key with state “Compromised” and re-key the key. Try to obtain a lease on the old key which fails. Locate the new key with the original name. Get the new key and obtain a lease.

| Time | Client A | Client B |
| --- | --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’, Name={ NameValue=‘ rekeyKey’, NameType=’00000001’ }, ActivationDate=’2’ } Out: objectType=’00000002’, uuidKey |  |
| 1 | Get (symmetric key) In: uuidKey Out: objectType = ‘00000002’, uuidKey, symmetricKey |  |
| 2 | Obtain Lease In: uuidKey Out: uuidKey, leaseTime, lastChangeDate |  |
| 3 |  | Revoke (symmetric key as compromised) In: uuidKey, RevocationReason=’00000002’, CompromiseOccurrenceDate=’6’ Out: uuidKey |
| 4 |  | Rekey In: uuidKey, offset=’0’ Out: uuidNewKey |
| 5 | Obtain Lease In: uuidKey Out: Operation Failed, Permission Denied |  |
| 6 | Locate (symmetric key) In: attributes={ Name={ NameValue=‘rekeyKey’, NameType=’00000001’ } } Out: uuidNewKey |  |
| 7 | Get (symmetric key) In: uuidNewKey Out: objectType = ‘00000002’, uuidNewKey, newSymmetricKey |  |
| 8 | Obtain Lease In: uuidNewKey Out: uuidNewKey, leaseTime, lastChangeDate |  |
| 9 | Destroy In: uuidKey Out: uuidKey |  |
| 10 | Destroy In: uuidNewKey Out: uuidNewKey |  |

# Archival

These use-cases test archiving and locating keys using the off-line indicator. If the server performs the Archive and Recover operations asynchronously, the client Polls the server until the operations complete. The client indicates in the request that it supports asynchronous responses.

## Use-case: Create a Key, Archive and Recover it

Create a symmetric key with a specified name, then use Locate to find the key and get the key. Archive the key (asynchronous operation, use Poll until it completes) and use Get and Locate on it, but both fail. Add the Storage Status Mask to the Locate-command, indicating to the server to search in both online and archived storage. The Locate finds the key. Recover the key from the archive (also asynchronous), both Locate and Get succeed.

| Time | Client A |
| --- | --- |
| 0 | Create (symmetric key) In: objectType=’00000002’, attributes={ CryptographicAlgorithm=’AES’, CryptographicLength=’128’, CryptographicUsageMask=‘0000000C’, Name={ NameValue=‘archiveKey’, NameType=’00000001’ } } Out: objectType=’00000002’, uuidKey |
| 1 | Locate In: attributes={ Name={ NameValue=‘archiveKey’, NameType=’00000001’ } } Out: uuidKey |
| 2 | Get (symmetric key) In: uuidKey Out: objectType = ‘00000002’, uuidKey, symmetricKey |
| 3 | Archive In: uuidKey, asynchronousIndicator=’true’ Out: asynchronousCorrelationValue |
| 4 | Poll* In: asynchronousCorrelationValue Out: uuidKey |
| 5 | Get (symmetric key) In: uuidKey Out: Operation Failed, Item Not Found |
| 6 | Locate In: attributes={ Name={ NameValue=‘archiveKey’, NameType=’00000001’ } } Out: Operation Failed, Item Not Found |
| 7 | Locate In: storageStatusMask=’00000003’, attributes={ Name={ NameValue=‘archiveKey’, NameType=’00000001’ } } Out: uuidKey |
| 8 | Recover In: uuidKey, asynchronousIndicator=’true’ Out: asynchronousCorrelationValue |
| 9 | Poll* In: asynchronousCorrelationValue Out: uuidKey |
| 10 | Get (symmetric key) In: uuidKey Out: objectType = ‘00000002’, uuidKey, symmetricKey |
| 11 | Destroy In: uuidKey Out: uuidKey |

# Implementation Conformance

This document is intended to be informational only and as such has no conformance clauses. The conformance requirements for the KMIP specification can be found in the "KMIP Specification" document itself, at the URL noted on the cover page of this document.

Acknowledgments

The following individuals have participated in the creation of this specification and are gratefully acknowledged:

Original Authors of the initial contribution:

David Babcock, HP

Joseph Birr-Pixton, Thales/nCipher

Mathias Björkqvist, IBM (editor)

John Clark, HP

Stan Feather, HP

Jon Geater, nCipher

Bob Griffin, EMC

Robert Haas, IBM

Jack Harwood, EMC

Vlad Libershteyn, HP

Mark Lin, EMC/RSA

Brian Metzger, HP

Madhav Mutalik, EMC/RSA

Anthony Nadalin, IBM

René Pawlitzek, IBM (editor)

Bruce Rich, IBM

Parameswaran Seshan, EMC/RSA

John Tattan, EMC

Participants:

Gordon Arnold, IBM

Todd Arnold, IBM

Matthew Ball, Sun Microsystems

Elaine Barker, NIST

Peter Bartok, Venafi, Inc.

Mathias Björkqvist, IBM

Kevin Bocek, Thales e-Security

Kelley Burgin, National Security Agency

Jon Callas, PGP Corporation

Tom Clifford, Symantec Corp.

Graydon Dodson, Lexmark International Inc.

Chris Dunn, SafeNet, Inc.

Paul Earsy, SafeNet, Inc.

Stan Feather, HP

Indra Fitzgerald, HP

Alan Frindell, SafeNet, Inc.

Judith Furlong, EMC Corporation

Jonathan Geater, Thales e-Security

Robert Griffin, EMC Corporation

Robert Haas, IBM

Thomas Hardjono, M.I.T.

Marc Hocking, BeCrypt Ltd.

Larry Hofer, Emulex Corporation

Brandon Hoff, Emulex Corporation

Walt Hubis, LSI Corporation

Wyllys Ingersoll, Sun Microsystems

Jay Jacobs, Target Corporation

Glen Jaquette, IBM

Scott Kipp, Brocade Communications Systems, Inc.

David Lawson, Emulex Corporation

Robert Lockhart, Thales e-Security

Shyam Mankala, EMC Corporation

Marc Massar, Individual

Don McAlister, Associate

Hyrum Mills, Mitre Corporation

Landon Noll, Cisco Systems, Inc.

René Pawlitzek, IBM

Rob Philpott, EMC Corporation

Bruce Rich, IBM

Scott Rotondo, Sun Microsystems

Anil Saldhana, Red Hat

Subhash Sankuratripati, NetApp

Mark Schiller, HP

Jitendra Singh, Brocade Communications Systems, Inc.

Servesh Singh, EMC Corporation

Sandy Stewart, Sun Microsystems

Marcus Streets, Thales e-Security

Brett Thompson, SafeNet, Inc.

Benjamin Tomhave, Individual

Sean Turner, IECA, Inc.

Paul Turner, Venafi, Inc.

Marko Vukolic, IBM

Rod Wideman, Quantum Corporation

Steven Wierenga, HP

Peter Yee, EMC Corporation

Krishna Yellepeddy, IBM

Peter Zelechoski, Associate

Revision History

| Revision | Date | Editor | Changes Made |
| --- | --- | --- | --- |
| ed-0.98 | 2009-04-28 | Mathias Björkqvist | Initial conversion of input document to OASIS format. |
| ed-0.98 | 2009-08-06 | Mathias Björkqvist | Changes to layout and message content to reflect the recent changes to the KMIP specification, added descriptions to the use-cases for which they were missing. |
| ed-0.98 | 2009-09-28 | Mathias Björkqvist | Updated messages and TTLV encodings to conform with KMIP specification ed-0.98 rev 17. |
| draft-01 | 2009-10-08 | Mathias Björkqvist | Removed normative words “must”, “shall”, “required”, “will” and “can”; updated messages and TTLV encodings to conform to KMIP specification ed-0.98 rev 19; added normative references; added minor edits |
| draft-02 | 2009-10-15 | Mathias Björkqvist | Replaced the TBDs, changed status to Committee Draft, changed use-cases to use protocol major version 1 and minor version 0 |
| draft-03 | 2009-10-15 | Mathias Björkqvist | Corrected names of TC chairs |
| draft-04 | 2009-11-05 | Mathias Björkqvist | Added list of participants, added reference to Profiles document, line spacing change to list of original contributors, added related documents |
| cd-05 | 2009-11-06 | Mathias Björkqvist | Changes to various naming aspects on front page and document footer. This is the tentative version for public review. |